On-Site Live HV Work Technique Review (G&B)

Team Members………………………………………………………………………………………………………………

Job Location…………………………………………………………………………………………………………………

Task……………………………………………………………………………………………………………………………

Date……/………/…….

| No. | Task/Technique | Compliance | Comments |
| --- | --- | --- | --- |
|  |  | Yes | No | N/A |  |
|  | Undertake Hazard & Risk assessment Voltage identification Structure security/soundness inc adjacent poles Manage step & Touch potential Communication link to control room available Live Line protection enabled Traffic and pedestrian control Safe to approach test (SWER) |  |  |  |  |
|  | Use of conductor support sticks Clean/prepare for use Inspect sticks and brackets for problems. Check within test. Setting of MAD markers. Check operation of conductor support brackets |  |  |  | Next Test Date: / / |
|  | Use of insulating barriers and covers Clean/prepare for use Inspect insulation for damage. Check within test date. Correct Voltage Class being used. Drop zone covered Cover connectors checked for no damage |  |  |  | Next Test Date: / / |

| No. | Task/Technique | Compliance | Comments |
| --- | --- | --- | --- |
|  |  | Yes | No | N/A | Comments |
|  | Use Insulating Gloves and Sleeves Inspect for damage inside and out and air test Inspect Outer leather Glove Clean prior to use Check for fitting/overlap between G&S Correct Class of G&S selected Check within test date |  |  |  | Next Test Date: / / |
|  | Act as a Safety Observer Concentration maintained Effective Communication with crew aloft Positioned to view personnel aloft Vest/identification worn. Verbalised warning for crew aloft if applicable |  |  |  |  |
|  | Effective Team communication Explanation of tasks to be completed. Clear directions given to ground crew. Acknowledgement of task completion Discussion of diversion from original work plan. |  |  |  |  |
|  | Load taken on insulating sticks correctly. Calculation of conductor load SWL of support sticks/rig not exceeded Correctly rigged as per manuals/manufactures procedures |  |  |  |  |
|  | Live Line rope management. Inspection of rope for problems. Correct knotting used. Insulators used in taglines/headropes. Dry ropes used. Ropes tested where applicable |  |  |  |  |
|  | Use Fall Prevention Equipment. Inspected prior to use. Correct adjustment of harness Lanyard attached with energy absorber end to fall arrest point of harness. Dry lanyards used. Within inspection date |  |  |  | Next Inspection Date: / / |

| No. | Task/Technique | Compliance | Comments |
| --- | --- | --- | --- |
|  |  | Yes | No | N/A | Comments |
|  | Use EWP Prestart checks completed. Within Electrical Test Secondary EWP controls working Escape devices present Ground person aware of rescue methods EWP chassis Earthed Clearances from uninsulated parts maintained. Insulated section cleaned and inspected. Clearance from lower circuit managed. Drop zone covered if clearance cant be maintained. SWL not exceeded Hydraulic tool hose condition / test date |  |  |  | Next Test Date: / / Next Test Date: / / |
|  | Working with Cranes Correct signals or standard terminology used. One person direction of Crane operator. Clear directions conveyed between persons aloft and ground man. |  |  |  |  |

| No. | Task/Technique | Compliance | Comments |
| --- | --- | --- | --- |
|  |  | Yes | No | N/A | Comments |
|  | Make /Break bridges Load switching device used correctly Current loading identified /measured-checked for removal of load. Load break components checked prior to installation Jumper movement controlled/considered. Connections cleaned before jointing. Correct connectors used &installed in correct orientation. 1.6km distance not exceeded |  |  |  |  |
|  | Minimum Approach Distances not breached. MAD correctly selected Body positioning for task adequate EWP/Platform placement adequate Mobile plant used not breaking MAD Covering used on conductors and structures appropriate to task. |  |  |  | Voltage /mm Kv /mm |
|  | Conductor repair. Assessment of structural condition. Application of tension devices Correct helical terminations or comealongs used. Correct sleeve and crimping Dies used Loading through circuit considered and appropriate jumper lead configuration /connection used Adequate covering applied to other conductors and structure. Drop zone covered Conductors cleaned before jointing |  |  |  |  |

|  | Install/remove mid Span Isolators Check for correct operation. Contacts & Arc break Correct helical terminations selected. Correct sleeve and crimping Dies used Loading through circuit considered and appropriate lead configuration /connection used Check turnbuckle for mechanical operation Contact closed and lead connections made before conductor cut.. check with safety observer for go ahead. Adequate covering applied to other conductors and structure. Vertical application install bottom first. Drop zone covered Conductors cleaned before jointing |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Crossarm Replacement Intermediate Angle Termination Correct helical terminations selected Load change considered on adjacent structures |  |  |  |  |

## General Comments: